6 | 10 | 20 | 40 | 60 W Chassis-Mount DC-DC Converters with 80-160Vin for Harsh Environments
with 3kVAC Reinforced I/O Isolation and Internal EN 55032 / EN 55035 Class A Filter

San Jose, Calif. – February 4, 2020:  TRACO POWER announces the release of the TMDC-H family of chassis-mount DC-DC converter modules covering 5 power levels ranging from 6~60 watts featuring 80~160 VDC input ranges and 3kVAC reinforced I/O isolation making them ideal for rugged environments and industrial applications.

The TMDC-H modules come fully encapsulated with terminal strip connections for ease of installation in industrial applications and equipped with integrated filters limiting emissions (EN 55032 class A) and immunity (EN 55035) without the need for external components.  Each wattage level consists of 8 different models offering 80-160 VDC input ranges and outputs of 5 / 12 / 15 / 24 / 48 / ±12 / ±15 / ±24 VDC with high efficiency operation up to 89%.  Features include: Remote ON/Off control; Power Good LED indicator; full-load convection-cooled operation from -40°C to +85°C (model dependent); high reliability with an MTBF of >4.1 million hours supported by a 3 year warranty; and international safety approvals to UL/EN 62368-1 with CB Report.  Optional DIN Rail mounting kits make these ideal for industrial control cabinets.

Products are in stock and available through distributors around the globe with manufacturing lead times of 12-14 weeks.  Please see www.tracopower.us/tmdc-h for specifications, drawings and safety documentation.

For further information and reader enquiries:

Paul Christiansen, TRACO Power North America, Inc.

2025 Gateway Place #330, San Jose, CA 95110

Office: +1 (408) 916-4570	Email:  p.christiansen@tracopower.com

Fax:    +1 (408) 916-4571

For further information, text and graphics by email or to discuss feature article opportunities:

Gorden Mack, Info-Mgt.net, 34786 Blackstone Way, Fremont CA 94555

Tel:	(408) 821-8283			E-mail:	gmack@info-mgt.net

Note to editors:

Power supply specialists, Traco Power is headquartered in Baar, Switzerland. Offering more than 25 years of experience in power, Traco Power is dedicated to the design and manufacture of high-quality DC/DC and AC/DC power conversion products. Traco Power’s mission is to provide customers with the optimal power supply solution in terms of performance, quality and price. Traco Power’s commitment to quality is supported by a 3 or 5 year product warranty on all products.